PikeMQ Messaging Protocol
Version 0.1

## What is PikeMQ
PikeMQ is designed as lightweight a subset of MQTT (at least featurewise!). In contrast to most MQTT implementations the idea of Pike is not to have a large-scale capable infrastructure, but instead to have a simple lightweight library, that empowers applications to take on the serverrole without the need for additional infrastructure.
In order to preserve the intended simplicity of the protocol and the libraries some of the features known from MQTT have been omitted, most notably:
- Persistent sessions
- Retained Messages
In general Pike uses very similar structures to MQTT while trying to remove complexity where appropriate, an also to tackle some of the – perceived – deficiencies of MQTT.
# Frametypes
- Connect
  - ConAck
  - ConRefused
- Publish
  - PubAck
  - PubRefused
- Subscribe
  - SubAck
  - SubRefused
- Unsub
  - UnsubAck
- Disconnect
- Ping
  - PingAck

## Encoding
Type	Code
Connect	0x01
ConReply (Ack/Nack)	0x02
Publish	0x03
PubReply (Ack/Nack)	0x04
Subscribe	0x08
SubReply (Ack/Nack)	0x09
Unsub	0x0A
UnsubReply	0x0B
Ping	0x0C
PingAck	0x0D
Disconnect	0x0E
ChannelEvent	0x0F
EventAck	0x10
RFU	0x00

## Length Encoding (Multi-Byte-Encoding)
In contrast to MQTT we skip on the rather complicated encoding of lengths in favor of just using 2 Bytes, resulting in a maximum framelength of 2^16 Bytes.
## Channel/Topic Names
A channel/topic name can be any valid UTF-8 string with a maximum length of 16k characters.

## Security
PikeMQ offers basic options for security, meaning, that the connection frame offers a field that can be used to indicate an encryption setting (e.g. by sending the index of a key in a given keystore). This boils down to two things:
- Pike embedded security can only use stream ciphers. All Pike implementations shall assume, that the full payload of all frames is encrypted, i.e. all data except the leading STX + Frame length and the trailing ETX.
- If advanced security is required, use OS supplied point to point connections (e.g. IPSEC)
Pike also does not provide the Username/Password feature that is present in MQTT by default, however it can be implemented by applications using Pike without protocol modifications by supplying Username + Password in the SecData field of the connection request. Note, that the connection request will usually never be encrypted, so this is pseudo-secure (or: at least not more or less secure than basic MQTT).

## Quality of Service
The quality of service setting for each published message has the following meaning
#### “Best Effort”
The server will not ACK the message and just relay it to any clients listening on the channel. If nobody is listening, the message will be discarded, if the server had no capacity to dispatch the message, it is discarded.
#### “Guaranteed Dispatch”
The server will explicitly ACK the message upon reception. The client can be sure, that the message will be dispatched by the server. However: If nobody is listening, the message will be discarded
#### “Guaranteed Delivery”
The server will ACK the message, if at least one recipient is present. If nobody is listening, the server will send a NACK with an additional flag, to denote this.
Note, that nothing is queued ever – the server is allowed to use internal queues in order to organize sending of messages, but it shall not try to be a memory for connecting clients.

## Basic Framelayout
STX	Frame length	TTL (?)	Frame type	Frame specific Data	ETX

The length is a multibyte thingy and includes all following data except the ETX.

## The Connect Frame
Protocolversion	Client ID	Security Data Len	Security Data	LastWillChanLen	LastWillChan	Lastwill Length	Lastwill Message
1 Byte, 0x01, as of now	Max 16 Byte, 0x00 terminated.	2 Byte	SecData Len byte	2 Byte	ChanLen Bytes	2 Byte	lastWillLength Bytes

The security data field can be used for a custom security implementation, e.g. by using it to index into a keystore to retrieve the key for a symmetric cipher.
TBD: Password? Security?
## ConReply Frame, Data
Status Code
1 Byte

Valid Codes:
- 0x00  Connection Established
- 0x01  Connection Refused, Bad Protocolversion
- 0x02 Connection refused, bad credentials (i.e. client id was blocked or similar)
- 0xFF  Connection Refused, General Error.

## The Publish Frame
QoS	MessageID	ChanLen	ChanId	PayloadLen	PayloadData
Any Valid QoS Setting	4 Byte	2 Byte	ChannelId, ChanLen Bytes	2 Byte	PayloadLenByte

Valid QoS Settings:
- 0x01  Best Efford
- 0x02  Guaranteed delivery
- 0x03  Guaranteed dispatch
The publish frame is sent from a given client to the broker. The broker itself shall use the “Channel Event” frame to relay the message to any interesting clients.
## Publish Reply Frame
MessageID	StatusCode
4 Byte	1 Byte

Status Codes:
- 0x00  ACK (Dispatch): Message accepted by server, dispatch will be attempted.
- 0x01 NACK (Dispatch): Server cannot handle message right now and did not accept.
- 0x03ACK (DELIVERY): Server was able to deliver the message to at least one other client
- 0x04NACK (Delivery): Server as unable to deliver the message, b/c. nobody was listening.
Note, that QoS 0x03 may send status code 0x01 as well, if the server currently has no resources to handle the message.
Also note, that in case of QoS 0x01 no reply will be sent by the server.

## The Subscribe Frame
ChanLen	ChanID
2 Byte	ChanLen Bytes

## The Subscribe Reply Frame
ChanLen	ChanID	Status
2 Byte	ChanLen Bytes

Value of status:
- 0x00  Success
- 0x01  Failed due to missing authorization.
- 0xFF  General error (unspecified)

## The Unsubscribe Frame
ChanLen	ChanID
2 Byte	ChanLen Bytes

## The Unsubscribe Reply Frame
ChanLen	ChanID
2 Byte	ChanLen Bytes

## The Disconnect Frame
This frame has no payload.
## The Ping Frame
This frame has no payload.
## The Ping Reply Frame
This frame has no payload.
## The ChannelEvent Frame
Flags	MessageID	SrcClientID	ChanLen	ChanId	PayloadLen	PayloadData
1 Byte	4 Byte	4 Byte	2 Byte	ChannelId, ChanLen Bytes	2 Byte	PayloadLenByte

Flagbits:
b00000001: Request ACK: If this bit is set, the client receiving the message shall send an explicit ACK.
Other Bits: RFU

## The EventAck Frame
MessageId	Status
4 Byte	1 Byte

Valid Status Codes:
- 0x00: Message received
- 0x01: Service Oversaturated, try again later.
- 0xFF: Generic Error
Any broker, that receives Status 0x01 shall buffer the message and use binary exponential back off before trying to send the message again, giving the client time to recover. I.e.:
1st retry after 100 ms
2nd retry after 200 ms
3rd retry after 400 ms
5th retry after 500 ms
The broker may cancel resending the message after 5 retries.

##### Packet Order
The protocol does not give any guarantees on the order in which packets are sent to a client for all packets using QoS 0 or 1. For all packets using QoS 2 the broker shall stop dispatching further packets to a client until either the QoS 2 packet was ACK’d or the connection timed out.
## Direct Adressing
Each node shall be directly addressable by using the Client Identifier as a prefix for a channel, i.e.:
Channelname = “SomeChannel”  Dispatched to all nodes subscribing to “SomeChannel”
Channelname=”$NodeID/SomeChannel”  Dispatchted to NodeID.

##### Network Topology
PikeMQ is a graph topology at its core. This means, that each node in Pike can have one or several upstream nodes. To ensure delivery across multiple nodes the following assumptions are taken:
- Each subscription/unsub of a node is propagated to all upstream nodes,
- Upstream nodes will route messages to all subscribers, irrespective of the actual depth.
- Dedicated client nodes don’t need to provide server functionality.
- Servernodes are clients to their upstreams and servers to any node that connects to them and assumes the client role.
- QoS is satisfied to the next upstream node.
Results:
- All nodes can always talk to the nodes below them due to the routing feature
- All nodes can always talk to their siblings
- Easy loadbalancing with specialized nodes.