PikeMQ Messaging Protocol
Version 0.1

## What is PikeMQ
PikeMQ is designed as lightweight a subset of MQTT (at least featurewise!). In contrast to most MQTT implementations the idea of Pike is not to have a large-scale capable infrastructure, but instead to have a simple lightweight library, that empowers applications to take on the serverrole without the need for additional infrastructure.
In order to preserve the intended simplicity of the protocol and the libraries some of the features known from MQTT have been omitted, most notably:
- Persistent sessions
- Retained Messages
In general Pike uses very similar structures to MQTT while trying to remove complexity where appropriate.
# Frametypes
- Connect
  - ConAck
  - ConRefused
- Publish
  - PubAck
  - PubRefused
- Subscribe
  - SubAck
  - SubRefused
- Unsub
  - UnsubAck
- Disconnect
- Ping
  - PingAck

## Encoding
Type	Code
Connect	0x1
ConReply (Ack/Nack)	0x2
Publish	0x3
PubReply (Ack/Nack)	0x4
Subscribe	0x8
SubReply (Ack/Nack)	0x9
Unsub	0xA
UnsubReply	0xB
Ping	0xC
PingAck	0xD
Disconnect	0xE
RFU	0x0, 0xF

# Length Encoding (Multi-Byte-Encoding)
Similar, to MQTT, i.e: Upper Bit designates, that more data is following, i.e:
0	1	2	3	4	5	6	7	Len
0	0	0	0	0	0	1	1	3 Byte

0	1	2	3	4	5	6	7	Len
1	0	0	0	0	0	1	1	3 Byte + 1 Length Byte following
0	0	0	0	0	0	0	1

Total of above example (b0000011 << 7) + (b0000001) = 0x181 = 385 Byte

## Channel/Topic Names
A channel/topic name can be any valid UTF-8 string with a maximum length of 16k characters.

## Security
PikeMQ offers basic options for security, meaning, that the connection frame offers a field that can be used to indicate an encryption setting (e.g. by sending the index of a key in a given keystore). This boils down to two things:
- Pike embedded security can only use stream ciphers. All Pike implementations shall assume, that the full payload of all frames is encrypted, i.e. all data except the leading STX + Frame length and the trailing ETX.
- If advanced security is required, use OS supplied point to point connections (e.g. IPSEC)
Pike also does not provide the Username/Password feature that is present in MQTT by default, however it can be implemented by applications using Pike without protocol modifications by supplying Username + Password in the SecData field of the connection request. Note, that the connection request will usually never be encrypted, so this is pseudo-secure (or: at least not more or less secure than basic MQTT).

## Quality of Service
The quality of service setting for each published message has the following meaning
“Best Effort”
The server will not ACK the message and just relay it to any clients listening on the channel. If nobody is listening, the message will be discarded, if the server had no capacity to dispatch the message, it is discarded.
“Guaranteed Dispatch”
The server will explicitly ACK the message upon reception. The client can be sure, that the message will be dispatched by the server. However: If nobody is listening, the message will be discarded
“Guaranteed Delivery”
The server will ACK the message, if at least one recipient is present. If nobody is listening, the server will send a NACK with an additional flag, to denote this.
Note, that nothing is queued ever – the server is allowed to use internal queues in order to organize sending of messages, but it shall not try to be a memory for connecting clients.

## Basic Framelayout
STX	Frame length	TTL (?)	Frame type	Frame specific Data	ETX

The length is a multibyte thingy and includes all following data except the ETX.

## The Connect Frame
Protocolversion	Client ID	Security Data Len	Security Data	LastWillChanLen	LastWillChan	Lastwill Length	Lastwill Message
1 Byte, 0x01, as of now	Max 16 Byte, 0x00 terminated.	MultiByte	SecData Len byte	MultiByte	ChanLen Bytes	MultiByte	lastWillLength Bytes

The security data field can be used for a custom security implementation, e.g. by using it to index into a keystore to retrieve the key for a symmetric cipher.
TBD: Password? Security?
## ConReply Frame, Data
Status Code
1 Byte

Valid Codes:
0x00  Connection Established
0x01  Connection Refused, Bad Protocolversion
0xFF  Connection Refused, General Error.

## The Publish Frame
QoS	MessageID	ChanLen	ChanId	PayloadLen	PayloadData
Any Valid QoS Setting	4 Byte	MultiByte	ChannelId, ChanLen Bytes	MultiByte	PayloadLenByte

Valid QoS Settings:
0x01  Best Efford
0x02  Guaranteed delivery
0x03  Guaranteed dispatch

## Publish Reply Frame
MessageID	StatusCode
4 Byte	1 Byte

Status Codes:
- 0x00  ACK (Dispatch): Message accepted by server, dispatch will be attempted.
- 0x01 NACK (Dispatch): Server cannot handle message right now and did not accept.
- 0x03ACK (DELIVERY): Server was able to deliver the message to at least one other client
- 0x04NACK (Delivery): Server as unable to deliver the message, b/c. nobody was listening.
Note, that QoS 0x03 may send status code 0x01 as well, if the server currently has no resources to handle the message.
Also note, that in case of QoS 0x01 no reply will be sent by the server.

## The Subscribe Frame
ChanLen	ChanID
MultiByte	ChanLen Bytes

## The Subscribe Reply Frame
ChanLen	ChanID	Status
MultiByte	ChanLen Bytes

Value of status:
0x00  Success
0x01  Failed due to missing authorization.
0xFF  General error (unspecified)

## The Unsubscribe Frame
ChanLen	ChanID
MultiByte	ChanLen Bytes

## The Unsubscribe Reply Frame
ChanLen	ChanID
MultiByte	ChanLen Bytes

## The Disconnect Frame
This frame has no payload.
## The Ping Frame
This frame has no payload.
## The Ping Reply Frame
This frame has no payload.

##### Network Topology
PikeMQ is a graph topology at its core. This means, that each node in Pike can have one or several upstream nodes. To ensure delivery across multiple nodes the following assumptions are taken:
- Each subscription/unsub of a node is propagated to all upstream nodes,
- Upstream nodes will route messages to all subscribers, irrespective of the actual depth.
- Dedicated client nodes don’t need to provide server functionality.
- Servernodes are clients to their upstreams and servers to any node that connects to them and assumes the client role.
- QoS is satisfied to the next upstream node.
Results:
- All nodes can always talk to the nodes below them due to the routing feature
- All nodes can always talk to their siblings
- Easy loadbalancing with specialized nodes.